## Slide 1: ArrayTrack: A Fine-Grained Indoor Location System
Jie Xiong, Kyle Jamieson
University College London
April 3rd, 2013
USENIX NSDI ‘13

## Slide 2: Precise location systems are important
Outdoors: GPS
  Accurate for navigation (meters)
  Signals fade in indoor environments
Precise and rapid indoor location enables:
Augmented reality on the smartphone, wearable or glasses
Fine-grained location in supermarkets, libraries or museums
Controlling network access based on desk or room
Known technologies: not accurate enough (WiFi), require dedicated infrastructure (ultrasound) or require cameras and good light conditions (vision)
2

## Slide 3: Timeline of indoor location systems
5.4 m (TIX) Gwon et al
39-51cm (Horus) Youssef et al
1 m (PinLoc) Sen et al
23 cm (ArrayTrack)
2 m (EZ)
Chintalapudi et al
30 cm (image-based) Hile and Boriello
3 cm (Bat) Ward et al
2-3 m (RADAR)
Bahl et al
5-10 cm (Cricket) Priyantha et al
97 cm (PinPoint) Joshi et al
1.2-4 m (Zee)
Rai et al
1992
>1 m (Badge) Want et al
1997
3
2000
2004
2005
2008
2010
2012
2013
time

## Slide 4: Two observations about WiFi
Increasing number of antennas on an access point (AP)
  802.11n MIMO links: improve capacity and coverage
  Draft 802.11ac (2014): 8 MIMO spatial streams (8 antennas)
Cisco Aironet 3600
Cisco Aironet 1250
RUCKUS ZoneFlex 7982
Xirrus XR7630
4 antennas
6 antennas
14 antennas
16 antennas
Motorola AP8132
4

## Slide 5: Two observations about WiFi
Increasing number of antennas on an access point (AP)
  802.11n MIMO links: improve capacity and coverage
  Draft 802.11ac (2014): eight MIMO spatial streams
WiFi is ubiquitous and densely deployed
  WiFi is now available on airplanes, subways and buses
  APs density is ever-increasing in the urban environment
5

## Slide 6: Our Approach
AP overhears a client’s transmission
AP leverages multiple antennas to generate physical angles of arrival (AoA) of a client's signals:
– AoA spectrum: power versus bearing at one AP
With multiple APs, central server synthesizes AoA spectra to obtain a location estimate for the client
AP 1
Client
AP 2
6

## Slide 7: Basic theory of operation
2πd/λ
Q
x1
I
Measured baseband signal at AP
Client
d
AP x1
λ
7

## Slide 8: Basic theory of operation
⎟
⎠
⎜
⎝
⎛

2
  arcsin
x  x1 ⎞
2πd/λ
Q
x1
I
x2
Client
θ
d θ
x1
x2
½λ sin θ
AP
λ/2
In a solely line-of-sight environment, phase measurements give client’s bearing to AP θ
8

## Slide 9: The challenge: multipath reflections
Problem #1: Strong multipath reflections indoors
Problem #2: Direct path attenuated or completely blocked
– Direct path signal may not be the strongest
Array
AoA spectrum
Client
AP
Wall
Furniture
0.2
0.4
0.6
0.8
1

## Slide 10: ArrayTrack’s multipath suppression algorithm
Key observation: direct path bearing is more stable than reflection path bearings when client moves slightly
array
AP
Client

## Slide 11: ArrayTrack’s multipath suppression algorithm
Given: AoA spectra from two nearby locations
Find the peak bearings in each AoA spectrum
Discard any peak not paired with a peak in the other AoA spectrum
Two peak bearings within five degrees are considered paired
✔

## Slide 12: Step 1: detection and recording
Content of packet and modulation type do not matter
Works with any part of a packet
– ArrayTrack utilizes the most robust preamble part
G
3.2 µs
800 ns
3.2 µs
12
10 short training symbols two long trainning symbols
Preamble

## Slide 13: Step 1: detection and recording
Very small part of a packet needed
– For a 40 MHz sampling rate, one sample is 25 ns
 |  |  | Packet body
0.5
30
240
190
300
0
N =1
0.5
60 120 60
120
150
180
150 30
180 0
N =5
1 90
0.5
60
120
150
In the absence of noise, one sample works
Employ multiple samples for
30
averaging to remove noise
0
N =10
1 90
0.5
Preamble part
30
60
120
150
180
180 0
N =100
190

## Slide 14: Step 1: detection and recording
 | 1 |  | 2 | Packet body
Port 1
Radio
Port 2
Diversity synthesis: existing 802.11 radios record the 1st half of the preamble from antenna 1 and the 2nd half from antenna 2
ArrayTrack’s diversity synthesis algorithm
  Record 10 samples from the first preamble half and another 10 samples from the second preamble half with different antennas
  Double the number of antennas we can utilize for ArrayTrack
antenna 1
Preamble part
antenna 2

## Slide 15: Step 2: AoA spectrum generation
x1 x2 x3 x4 x5 x6 x7 x8
0.5
30
60
90
120
150
NO spatial smoothing (SS)
1
MUSIC algorithm [Schmidt, 1986] for AoA spectrum estimation
– Does not work well for indoor environment because of coherent signals:
Transmitter
Receiver (Client)
(AP)
Spatial smoothing (SS) [Shan et al, 1985] handles coherent signals
0.5
30
60
90
1 120
150
SS with 2 sub−array groups
180
0
180
0

## Slide 16: Step 3: AoA spectra synthesis
N APs generate N AoA spectra
For a random position X, the likelihood of being at X is a multiplication of
probabilities from multiple APs
0.2
0.4
0.6
0.8
1
0.2
0.4
0.6
0.8
1
X
AP 2
AP 1
P(x2) =0.6
P(x1) =0.45
P(x) = P(x1) * P(x2)
16

## Slide 17: Step 4: search for highest probability position

## Slide 18: Implementation
AP: two WARPs, each with four radio boards (eight antennas)
  Custom FPGA design using Xilinx System Generator for packet synchronization, diversity synthesis, RF oscillator synchronization
  4-16 antennas placed in a linear arrangement, spaced at λ/2 (6.13 cm)
Clients: Soekris boxes equipped with 802.11 radios
Backend location server: implemented in Matlab (1,000+ LoC)

## Slide 19: Floorplan: client and AP positions
N
AP
Client
1
2
3
4
5
6
Backend server has knowledge of each AP’s location

## Slide 20: Evaluation
How accurate is MUSIC + SS?
ArrayTrack’s multipath suppression improvement
Effect of number of antennas on each AP
Effect of client-AP differences in height

## Slide 21: Effects of number of APs
Heatmap example of increasing number of APs
two APs
one AP three APs
four APs
five APs
six APs

## Slide 22: MUSIC + SS achieves 26 cm accuracy
In general, with increasing number of APs, more accurate location information can be obtained
22
1
50010002500
0
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0.8
0.9
1
5 10 20 50 100
Location error (cm)
CDF
6 APs (MUSIC + SS)
5 APs (MUSIC + SS)
4 APs (MUSIC + SS)
3 APs (MUSIC + SS)

## Slide 23: Evaluation
How accurate is MUSIC + SS?
ArrayTrack’s multipath suppression improvement
Effect of number of antennas on each AP
Effect of client-AP differences in height

## Slide 24: Multipath suppression improves accuracy
Median: 23 cm (ArrayTrack with 6 APs)
The fewer APs, the more important is multipath suppression
0
500
1000
1500 2000 2500
0
0.5
1
ArrayTrack (6 APs) MUSIC + SS (6 APs)
0
500
1000
0
0.5
1
ArrayTrack (5 APs) MUSIC + SS (5 APs)
1500 2000 2500
0
500
1000
1500 2000 2500
0
0.5
1
CDF
ArrayTrack (4 APs) MUSIC + SS (4 APs)
0
500
1000 1500 2000 2500
0
0.5
1
Location error (cm)
ArrayTrack (3 APs) MUSIC + SS (3 APs)
With multipath suppression, the long tail is removed

## Slide 25: Optimal subset of APs
1
2500
0
0.1
0.2
0.5
0.4
0.3
0.6
1
0.9
0.8
0.7
5 10 20 50 100 500
Location error (cm)
CDF
ArrayTrack (6 APs) Optimal subsets of APs MUSIC + SS (6 APs) MUSIC + SS (3 APs)
On average, 6 APs present the best result
It’s not true for a particular position
25
23 cm
2.5 cm

## Slide 26: Evaluation
Effect of number of APs on accuracy
Multipath suppression improvement
Effect of number of antennas on each AP
Effect of client-AP differences in height/orientation
26

## Slide 27: Number of antennas at AP
1
500
0
0.7
0.6
0.5
0.4
0.3
0.2
0.1
0.9
1
10 20 50 100
Location error (cm)
CDF
ArrayTrack 4−antenna APs ArrayTrack 6−antenna APs
ArrayTrack 8−antenna APs
0.8
27

## Slide 28: Evaluation
Effect of number of APs on accuracy
Multipath suppression improvement
Effect of number of antennas on each AP
Effect of client-AP differences in height

## Slide 29: High accuracy despite AP-client height difference
3 m
1.5 m
ceiling
1
100
0
0.2
0.4
0.6
0.8
1
10 20
Location error (cm)
CDF
Different antenna heights
Original

## Slide 30: Other characteristics of ArrayTrack
Small latency (1-3 packets needed )
Robust against low SNR
Robust against collision

## Slide 31: Conclusions
ArrayTrack: a robust, fast and responsive localization system with a median accuracy level of 23 cm (6 APs) and one meter (3 APs)
  Novel multipath suppression and diversity synthesis algorithms
  Uses only the WiFi infrastructure nearby
  Robust against low SNR and packet collisions
  Fast and responsive: requires only 1-3 packets
Three dimensional tracking with two-dimensional array for future work
Thank you!

## Slide 32: Implementation challenges
Wire connects WARPs to share the same sampling clock and RF oscillator
USRP2 calibrates WARPs to remove WARP internal phase offsets
Remove phase offsets due to hardware imperfections
  Cables labeled with the same lengths are not exactly the same
  SMA splitters are not fully balanced

## Slide 33: AP-client antenna orientations
1
100
0
0.2
0.4
0.6
1
10 20
Location error (cm)
CDF
Different antenna orientations
Different antenna heights
Original
0.8
33
Circularly-polarized antennas mitigate the performance drop